## Slide 1: Optimal Stochastic Control for Generalized Flow Problems
Abhishek Sinha
Joint work with
Prof. Eytan Modiano
LIDS, MIT

## Slide 2: Introduction
We consider the Generalized Flow Problem where the packets are to be routed in a network from their source to destinations at the maximum rate possible.
Packets may belong to different sessions including unicast, broadcast, multicast or anycast.
This is a fundamental problem with numerous applications: Internet routing, in-network function computations, live streaming and multimedia broadcasting, military communication etc.
Well-studied in the literature with problem specific algorithms- Unicast: Backpressure (Tassiulas, ‘92), (Wired) Broadcast (Massoulie, ‘08), (Tree-based) Multicast (Sarkar, ‘02)
Our contribution: A single, efficient and dynamic algorithmic paradigm that solves all problems and improves performance over the state-of-the-art.

## Slide 3: System Model
Multi-hop wireless network
  Only a subset of the links can be activated simultaneously, due to interference
Stochastic arrivals – i.i.d. process with arrival rates λij
  The λij’s are unknown in advance
Time-slotted system
λ12 , λ14 , λ16
2
1
3
5
6
4
7
8
λ21 , λ24 , λ28
λ6i , ...

## Slide 4: Arrivals and Link Scheduling: Example
Example – primary interference
2
1
3
6
4
7
8
6
6
6
6
7
6
7
7
6
7
7
6
7
7
6

## Slide 5
Traffic Classes: Class c packets has arrival rate , source node Sc, destination node(s), Dc, where,
Unicast: Single source, single destination
Multicast: Single source, multiple destinations
Broadcast: Single source, all destinations
Anycast: Single source, choice of one among alternative destinations
Traffic Classes: Generalized Flow

## Slide 6: Problem Statement
Given a wireless network , with packets arriving at source nodes according to an i.i.d process of rate
Objective: Find a routing and scheduling policy that will support all arrival rates within the network stability region
  Including a mix of unicast, multicast, broadcast, etc.
Unicast Problem: Find a routing and scheduling strategy to support any unicast rate
Broadcast Problem: Find a routing and scheduling strategy to support any broadcast rate
Similar definition for Multicast and Anycast

## Slide 7: Previous work and their limitations
The Backpressure algorithm (Tassiulas et al. ‘92) is throughput optimal for unicast traffic
Cannot be extended to other important problems - despite tremendous effort over the past 25 years
  Broadcast, Multicast, Anycast, etc.
We develop the first general framework that can be used to solve general network-flow problems with provable optimality guarantees
Our algorithm is fundamentally different from backpressure
  Avoids issues of looping in network
  Significant delay improvement over backpressure for unicast

## Slide 8: Our earlier work on this problem
Earlier we concentrated exclusively on the Broadcast problem
We obtained a throughput-optimal broadcast algorithm for wireless DAGs (Sinha, Li, Paschos, Modiano, INFOCOM’15 and TON ’16)
The algorithm used the idea of in-order delivery of packets in a certain restricted policy space. Activations was done using a Max-Weight scheme where the weights are a function of “last received packet indices” of nodes.
This policy was further generalized to time-varying graphs and broadcast capacity was explicitly characterized (Sinha, Tassiulas, Modiano, MobiHoc ’16)
We also obtained a different throughput-optimal broadcast policy for arbitrary networks (Sinha, Paschos, Modiano, Mobihoc ’16).
This policy used the idea of ‘backpressure on sets’. Also a natural heuristic was proposed using Multi-class in-order policy.

## Slide 9: What’s new ?
The Universal Max-Weight algorithm (UMW) differs fundamentally from the traditional Back-Pressure (BP) like algorithms in the following aspects:
Unlike BP which makes routing decisions for each packet hop-by-hop, UMW dynamically chooses routes for each packet at the source (source routing)
Unlike BP which makes routing and scheduling decisions based on queue-length information at nodes, UMW is oblivious to physical queue-lengths
UMW takes control actions based on virtual queue-lengths, which corresponds to a simpler precedence-relaxed system
UMW uses standard min-cost algorithms (e.g., Shortest path, MST, min-cost Steiner Tree etc.) at the sources

## Slide 10: Design of UMW: Insight
Because of mutual interdependence, networked queues are harder to analyze and control
This motivates us to obtain a relaxed system which is easier to analyze yet preserves fundamental characteristics (e.g., stability)
Idea : Relax Precedence constraints
Link 1
Link 2
Source
Destination

## Slide 11: Precedence Relaxed System
As an example, consider a two-hop network
  The packet p has to traverse both link 1 and 2 and to reach its destination
Equivalent virtual queue system (counter)
  Packet arrives to both queues symultaneously
p
Link 1
Link 2
p
p
p

## Slide 12: Virtual Queueing System : Operation
Associate a virtual queue with each link in the graph
Upon packet arrival:
  Determine a route (e.g., path, tree) for the packet to its destination(s)
  Immediately inject a new packet to each virtual queue (link) along the route
Packets are replicated to the virtual queues as soon as they arrive at the source
  Based on their chosen path
Packets are served from the virtual queues as long as the corresponding virtual queues are non-empty
  Subject to the scheduling constraints

## Slide 13: Packet Routing and Arrivals at the Virtual Queue
The physical route of a packet is chosen as soon as the packet arrives at the source
Depending on the type of flow, the routes take the following forms:
  Unicast:
  Broadcast :
  Multicast problems:
An incoming packet is injected into virtual queue iff the packet’s chosen route includes the edge e
Hence UMW uses source routing as opposed to hop-by-hop routing of backpressure
  Suitable for emerging SDN paradigm

## Slide 14: Controller Arrivals: Unicast Example
a
b
c
d
Qab
Qbd
Qac
Qcd
Qbc
+1
+1
Virtual Queues
Unicast arrival from a – d
Chosen path: a-c-d
Arrival to Qac and Qcd
a – d

## Slide 15: Controller Arrivals: Broadcast Example
a
b
c
d
Qab
Qbd
Qac
Qcd
Qbc
+1
+1
Virtual Queues
Broadcast arrival
Chosen tree: a-b-c-d
Arrival to Qac, Qab, and Qcd
p
+1

## Slide 16: Dynamics of the Virtual Queues
Define the controlled arrival vector to the virtual queue to be
where the controlled variable denotes number of virtual packet arrival at the virtual queue at time t
Let be the (controlled) departures from virtual queue at time t
The virtual Queues evolve according to the Lindley recursions:
Unlike the original system, given the controls, the virtual queues are independent of each other, making their control and analysis tractable

## Slide 17: Controlling the Virtual Queues
We next design a per-slot control policy which stabilizes the virtual queue-system
The policy consists of routing decisions: virtual queue arrivals and scheduling (link activation) decisions: virtual queue departures
Intuition: This control is likely to stabilize the physical queues as well
  However, note that the dynamics of the physical queues depends explicitly on the packet scheduling policy used within the queues (e.g., FCFS, etc.)
To stabilize the virtual queues, we choose a control which minimizes the drift of a Quadratic Lyapunov Function of the Virtual Queues
It turns out that the controls (routing, and link activations) are separable and reduces to standard combinatorial problems

## Slide 18: Derivation of the Control Policy
Define a Quadratic Lyapunov function
The one-slot drift of under policy is given by,
where and are respectively routing and activations chosen by the policy at time t
The drift upper-bound has nice separable form and may be minimized over the feasible controls separately

## Slide 19: Optimal Control: Routing
Minimizing the upper-bound on drift over the routing action, we get the following general route selection policy at time t
Special Cases:
  Unicast: Shortest path in the weighted graph
  Broadcast: Minimum weight Spanning Tree in
  Multicast: Minimum weight Steiner tree in , connecting the source node to the destination nodes

## Slide 20: Routing in the Virtual Network (example)
a
b
c
d
Qab =10
Qbd=15
Qac=5
Qcd=8
Qbc=7
10
15
5
8
7
Compute the Shortest Path
+1
+1
Virtual Queues

## Slide 21: Optimal Control: Link Scheduling
Similarly, minimizing the upper-bound on one-slot drift over link-scheduling actions we get the following activation policy:
Max-Weight activation, using virtual queue length
Example: For wireless networks with Primary interference constraints the above problem reduces to finding a Max-Weight-Matching in the weighted graph
Theorem (Stability of the Virtual Queues): With the above selection of Max-Weight controls, the virtual queue process is positive recurrent for any arrival rate vector in the interior of the stability region.
What does this tell us about the stability of the physical queues?
  Intuitively, we expect that the arrival rate is less than their departure rate

## Slide 22: Optimal Control: Packet Scheduling
How do we decide which packet to transmit over a link at any given time slot?
  Why does it matter? Can’t we just use FCFS?
Nearest to Origin (NTO) policy [Gamarnik, 1998]
Extended Nearest to Origin policy (ENTO): When multiple packets contend for an edge, schedule the one which has traversed the least number of edges
  Extension of NTO to general flow problems
  Theorem (Stability of the Physical Queues) : The overall UMW policy is throughput-optimal

## Slide 23: Proof of Stability of the Physical Queues
We have shown that the arrival rate to the physical links is less than the service rate
  Generally not enough for proving stability
The complete stability proof relies on a result from adversarial queueing theory {Gamarnic ‘98] for wired networks under NTO policy
We extend the proof to the wireless setting with ENTO
  Sample path argument
  Induction on the number of packets that are k-hops away from the origin:
    We show that the number of packets that are one hop away from origin is bounded, then use the condition from previous slide to show that the same holds for packets two hops away, etc.

## Slide 24: Analysis of the Physical Queues - I
Lemma: The virtual queues are almost surely rate-stable, i.e.
Hence for sample paths with , we have the bound
for some function
The above result enables us to analyze each sample path of the set separately and forms the key to our stability analysis of the physical queues.

## Slide 25: Analysis of the Physical Queues - II
For any edge define the cumulative arrival and service processes in the interval at the virtual queue as follows:
By the above definition, denotes total number of packets that have been injected into the virtual queue in the time interval .
However, from the description of UMW, this is exactly equal to the number of physical packets that have been injected into the network in the time interval that wish to cross the edge e in future. Denote this quantity by .
The same conclusion holds for the cumulative service process .

## Slide 26: Analysis of the Physical Queues - III
Using Theorem 1, the previous observation and Skorokhod Maps for the virtual queues, we obtain the following:
Theorem 2 : Almost surely for all sample paths , there exists a non-negative function such that for any the following holds for all physical queues:
The previous theorem informally states that the rate of arrival of packets at any edge is at most the rate of service offered to the edge almost surely, under the operation of the UMW policy.
Theorem 3 : Physical Queues are Rate Stable under ENTO.

## Slide 27: Simulation Results (Unicast)
Two Unicast flows : 1 to 8 and 5 to 2
Load Factor
Delay
UMW with virtual Queues
BP
UMW with Phy. Queues

## Slide 28: Simulation Results (Broadcast)
UMW with
Virtual Queues
UMW with
Phy. Queues

## Slide 29: Conclusion
Our understanding of network control theory has progressed enormously over the past 25 years, starting with the seminal work of Tassiulas and Ephremides in 1992.
Universal-Max-Weight is throughput optimal and can be used in a wide range of network flow problems
Universal-Max-Weight eliminates many of the drawbacks of the classical Back-Pressure algorithm
Open Problem: Does the proposed algorithm remain optimal when used in conjunction with the Physical Queue lengths, instead of the virtual queue-lengths ?
  Empirical evidence suggest yes
  Lead to a more efficient practical implementation of UMW